## Slide 1
Group Members
Honey Singh (1609731036)
Jaivardhan Sharma(1609731038)
Jayesh Singh(1609731041)
Krishn Gopal Dwivedi(1609731047)
GUIDE
Mr. Piyush Jain
MIMO FSO COMMUNICATION USING HYBRID SUBCARRIER INTENSITY MODULATION OVER
DOUBLE GENERALISED GAMMA FADING
DEPARTMENT OF ELECTRONIC AND COMMUNICATION ENGINEERING

## Slide 2
INTRODUCTION
MOTIVATION
OBJECTIVE
LITERATURE REVIEW
SYSTEM MODEL
MATHEMATICAL MODEL
RESULT AND DISCUSSION
CONCLUSION
PUBLICATION
REFERENCES
TABLE OF CONTENTS
2
FSO |

## Slide 3
Free-space optics (FSO) is wireless technology to transmit data through light waves.
It is Line of Sight (LOS) communication which uses narrow beam of light.
Some advantages of FSO are huge bandwidth , low power requirement and unlicensed spectrum.
FSO has other benefits like cost effectiveness, easy installation and maintenance.
It can be used in many areas like in military , space agencies ,difficult terrains etc.
INTRODUCTION
FSO |
3

## Slide 4
FSO have some shortcomings like fading , absorption and scattering of signal.
Major concern of FSO system is uncertainty in channel due to Atmospheric Turbulence.
Many statistical models have been proposed to model Atmospheric Turbulence.
These model are used to describe the PDF of irradiance fluctuation.
Some of these models are Negative exponential , Log Normal , and Gamma-Gamma.
Lognormal distribution widely used model but it analysis only weak turbulence.
We have used new statistical model Double Generalized Gamma distribution which is applicable to all turbulence conditions.
INTRODUCTION(CONTD.)
FSO |
4

## Slide 5
The modulation techniques can further be utilized to reduced the impact of turbulence.
There are different modulation techniques like PPM ,BPSK ,MPSK and OOK.
Power efficiency and data rate are important parameters for selection of modulation.
We have used Hybrid modulation which is combination of two or more modulation techniques. For example PPM-MPSK.
Using Hybrid LPPM-MPSK combines the advantages of PPM and MPSK
INTRODUCTION (contd.)
FSO |
5

## Slide 6
To achieve higher data rate with cost effectiveness FSO have been used.
FSO systems are also easy to deploy and maintain in difficult terrains.
Double GG distribution is proposed to model Atmospheric Turbulence under all conditions.
LPPM MPSK SIM Hybrid Modulation is used to combines the advantages of LPPM and MPSK SIM.
MIMO systems are used to mitigate the efforts are turbulence induced fading.
MOTIVATION
FSO |
6

## Slide 7
To model MIMO FSO Communication system with hybrid modulation technique over double generalized gamma distribution in the presence of the atmospheric turbulence-induced fading.
To analyze the effect of BER over average electrical SNR under various atmospheric turbulence conditions.
OBJECTIVE
FSO |
7

## Slide 8
LITERATURE REVIEW
FSO |
8
S.NO. | REFERENCES | FINDINGS | LIMITATIONS
1. | Yi, X., Yao, M. and Wang, X., 2017. MIMO FSO communication using subcarrier intensity modulation over double generalized gamma fading. Optics Communications, 382, pp.64-72.[1] | Average SER for SIM based MIMO FSO system is calculated. | BER performance of BPSK SIM is not analyzed which is better than MPSK SIM.
2. | Kashani , M.A., Uysal , M. and Kavehrad, M., 2015. A novel statistical channel model for turbulence-induced fading in free-space optical systems. Journal of Lightwave Technology, 33(11), pp.2303-2312.[2] | BER as well as outage probability of SIMO and SIMO FSO system. | No modulation technique is employed.
3. | Liu, H., Liao, R., Wei, Z., Hou, Z. and Qiao, Y., 2015. BER analysis of a hybrid modulation scheme based on PPM and MSK subcarrier intensity modulation. IEEE Photonics Journal, 7(4), pp.1-10.[3] | BER performance of PPM-MSK-SIM. | Log normal distribution is used which is applicable for weak turbulence conditions only.

## Slide 9
LITERATURE REVIEW (contd.)
FSO |
9
S.NO. | REFERENCES | FINDINGS | LIMITATIONS
4. | Giri, R.K. and Patnaik, B., 2019. Bit error rate performance analysis of hybrid subcarrier intensity modulation-based FSO with spatial diversity in various weather conditions. Journal of Optical Communications, 40(3), pp.307-314.[4] | BER of PPM MSK SIM. | BER performance for MIMO system is not analysed.
5. | AlQuwaiee, H., Ansari, I.S. and Alouini, M.S., 2016. On the maximum and minimum of double generalized gamma variates with applications to the performance of free-space optical communication systems. IEEE Transactions on Vehicular Technology, 65(11), pp.8822-8831.[5] | Average (BER) and the ergodic capacity (EC). | Weak turbulence condition is not analyzed.
6. | Kashani, M.A., Uysal, M. and Kavehrad, M., 2015, June. On the performance of MIMO FSO communications over double generalized gamma fading channels. In 2015 IEEE International Conference on Communications (ICC) (pp. 5144-5149). IEEE.[6] | BER performance of SIMO ,MISO and MIMO. | Weak turbulence condition is not analyzed.

## Slide 10
LITERATURE REVIEW (contd.)
FSO |
10
S.NO. | REFERENCES | FINDINGS | LIMITATIONS
7. | Aminikashani, M., Kavehrad, M. and Gu, W., 2016, February. Error performance analysis of FSO links with equal gain diversity receivers over double generalized gamma fading channels. In Broadband Access Communication Technologies X (Vol. 9772, p. 97720R). International Society for Optics and Photonics.[7] | BER performance of FSO with EGC is analyzed. | MIMO system is not considered.
8. | Jagadeesh, V.K., Palliyembil, V., Muthuchidambaranathan, P. and Bui, F.M., 2015. Free space optical communication using subcarrier intensity modulation through generalized turbulence channel with pointing error. Microwave and Optical Technology Letters, 57(8), pp.1958-1961.[8] | The effects of channel turbulence and pointing error are analyzed for BPSK-SIM FSO system. | BPSK-SIM is used but MPSK which is a better modulation scheme, is not analyzed. MIMO system is also not considered in this paper.

## Slide 11
LITERATURE REVIEW (contd.)
FSO |
11
S.NO. | REFERENCES | FINDINGS | LIMITATIONS
9. | Bhatnagar, M.R. and Ghassemlooy, Z., 2016. Performance analysis of gamma–gamma fading FSO MIMO links with pointing errors. Journal of Lightwave technology, 34(9), pp.2158-2169.[9] | Average SER is derived for both EGC and MRC. | Gamma-Gamma distribution is used which does not work for strong turbulence conditions.
10. | Li, J., Liu, J.Q. and Taylor, D.P., 2007. Optical communication using subcarrier PSK intensity modulation through atmospheric turbulence channels.[10] | The BER is derived for optical communication systems. | Log normal distribution is considered therefore strong turbulence condition is not analyzed.
11. | Kaur, P., Jain, V.K. and Kar, S., 2015. Performance analysis of free space optical links using multi-input multi-output and aperture averaging in presence of turbulence and various weather conditions. IET Communications, 9(8), pp.1104-1109.[11] | Performance of FSO link under various weather conditions is evaluated in terms of BER, outage probability and diversity gain. | Gamma-Gamma distribution is used which does not work for strong turbulence conditions.

## Slide 12
LITERATURE REVIEW (contd.)
FSO |
12
S.NO. | REFERENCES | FINDINGS | LIMITATIONS
12. | Saeed, R.A. and Abbas, E.B., 2018, August. Performance Evaluation of MIMO FSO Communication with Gamma-Gamma Turbulence Channel using Diversity Techniques. In 2018 International Conference on Computer, Control, Electrical, and Electronics Engineering (ICCCEEE) (pp. 1-5). IEEE.[12] | Examined the diversity combining techniques to minimize fading | Double generalized gamma distribution is not employed.
13. | Johnsi, A.A. and Saminadan, V., 2013, April. Performance of diversity combining techniques for fso-mimo system. In 2013 International Conference on Communication and Signal Processing (pp. 479-483). IEEE.[13] | Analyzed BER and outage probability for different combining techniques which increases system performance. | Log normal distribution is used which is applicable for weak turbulence conditions only.

## Slide 13
LITERATURE REVIEW (contd.)
FSO |
13
S.NO. | REFERENCES | FINDINGS | LIMITATIONS
14. | Saber, M.J. and Keshavarz, A., 2018, May. On performance of adaptive subcarrier intensity modulation over generalized FSO links. In Electrical Engineering (ICEE), Iranian Conference on (pp. 358-361). IEEE.[14] | Performance evaluation of adaptive subcarrier PSK intensity modulation over Malaga turbulence channel | PSK is used which has lower bandwidth efficiency.
15. | Sadiku, M.N., Musa, S.M. and Nelatury, S.R., 2016. Free space optical communications: An overview. European scientific journal, 12(9).[15] | Advantages and limitation of Free Space Optical communication. | -
16. | Vellakudiyan, J., Muthuchidambaranathan, P., Bui, F.M. and Palliyembil, V., 2015. Performance of a subcarrier intensity modulated differential phase-shift keying over generalized turbulence channel. AEU-International Journal of Electronics and Communications, 69(11), pp.1569-1573.[16] | Performance analysis of DPSK SIM based FSO system. Expression for BER, channel capacity and outage probability of the system. | DPSK is used which is highly sensitive to phase noise effects.

## Slide 14
LITERATURE REVIEW (contd.)
FSO |
14
S.NO. | REFERENCES | FINDINGS | LIMITATIONS
17. | Dabiri, M.T., Sadough, S.M.S. and Khalighi, M.A., 2017. FSO channel estimation for OOK modulation with APD receiver over atmospheric turbulence and pointing errors. Optics Communications, 402, pp.577-584.[17] | BER performance of EM channel estimator is analysed. | OOK modulation is used ,which offers lower power efficiency and is very susceptible to noise interference.
18. | Kaur, G., Singh, H. and Sappal, A.S., 2017. Free space optical using different modulation techniques—a review. International Journal of Engineering Trends and Technology (IJETT), 43(2).[18] | Methods for performance enhancement of FSO link are described . | DPIM and DPPM can also be employed.
19. | Popoola, W.O. and Ghassemlooy, Z., 2009. BPSK subcarrier intensity modulated free-space optical communications in atmospheric turbulence. Journal of Lightwave technology, 27(8), pp.967-973.[19] | The BER expression for SIM FSO is derived. | Spatial diversity is used which is only used for strong turbulence.

## Slide 15
LITERATURE REVIEW (contd.)
FSO |
15
S.NO. | REFERENCES | FINDINGS | LIMITATIONS
20. | Prabu, K. and Kumar, D.S., 2015. BER analysis for BPSK based SIM–FSO communication system over strong atmospheric turbulence with spatial diversity and pointing errors. Wireless Personal Communications, 81(3), pp.1143-1157.[26] | BER of BPSK-SIM based SISO and SIMO FSO systems over a strong atmospheric channel with pointing errors are derived. | MIMO system is not employed. Spatial diversity is used which is only used for strong turbulence.
21. | Ting Jiang, Lin Zhao ,Hong Zhang Liu Performance improvement for Mixed RF-FSO Communication System by Adopting Hybrid Subcarrier Intensity Modulation. MDPI Appl. Sci 2019 , 9,3724[27] | The BER expression of hybrid RF-FSO system | Spatial diversity is not considered.
22. | Faridzadeh, M., Gholami, A., Ghassemlooy, Z. and Gatri, A., 2014, September. BPSK-SIM-PPM modulation for free space optical communications. In 7'th International Symposium on Telecommunications (IST'2014) (pp. 794-798). | BER execution of the PPM-BPSK balance plot in the lognormal atmospheric channel. | BPSK-SIM is used but MPSK which is a better modulation scheme, is not analysed. MIMO system is also not considered in this paper

## Slide 16
LITERATURE REVIEW (contd.)
FSO |
16
S.NO. | REFERENCES | FINDINGS | LIMITATIONS
23. | Faridzadeh, M., Gholami, A., Ghassemlooy, Z. and Rajbhandari, S., 2012, July. Hybrid 2-PPM-BPSK-SIM with the spatial diversity for free space optical communications. In 2012 8th International Symposium on Communication Systems, Networks & Digital Signal Processing (CSNDSP) (pp. 1-5). IEEE.[29] | BER analysed for various combining techniques and found that system efficiency was increasing. | MIMO system is not MPSK-SIM is not analysed. Spatial Density is considered only for strong turbulence.
24. | Faridzadeh, M., Gholami, A., Ghassemlooy, Z. and Rajbhandari, S., 2012. Hybrid pulse position modulation and binary phase shift keying subcarrier intensity modulation for free space optics in a weak and saturated turbulence channel. JOSA A, 29(8), pp.1680-1685.[30] | The BER expression of hybrid RF-FSO system | Spatial diversity is not considered.

## Slide 17
LITERATURE REVIEW (contd.)
FSO |
17
S.NO. | REFERENCES | FINDINGS | LIMITATIONS
25. | Tiwari, Pawan, Nikhil Kumar, Pragati Singh, Chhavi Srivastava, M. Lakshmanan, Piyush Jain, and Saurabh Katiyar. "Modeling and Analysis of Hybrid SIM with L-PPM and MSK over Double Generalized Gamma Distribution in Free Space Optical Communication System." In 2019 International Conference on Vision Towards Emerging Trends in Communication and Networking (ViTECoN), 1-4. IEEE, 2019.[31] | BER performance of SISO FSO system for hybrid LPPM-MSK-SIM over double GG distribution under weak, moderate and strong turbulence conditions is analyzed. | MIMO FSO system is not considered.

## Slide 18
SYSTEM MODEL
FSO
Transmitter
(Hybrid LPPM MPSK-SIM Modulator)
FSO
Communication Channel
(Double GG Fading
Distribution)
FSO
Receiver
(Hybrid LPPM-MPSK-SIM Demodulator)
Input
Output
Fig 1.1. Block Diagram of Hybrid LPPM-MPSK-SIM communication system
FSO |
18

## Slide 19
MATHEMATICAL MODEL
FSO |
19
PDF OF DOUBLE GENERALIZED GAMMA DISTRIBUTION
The double Generalized distribution is obtained from Generalized Gamma Distribution of small scale and large-scale irradiance fluctuation 𝑎𝑛𝑑 modelled as and their PDFs are as follows,
(1.1)
(1.2)
where > 0, > 0.5 and , i = 1, 2 are the parameters of the generalized gamma distribution, is the irradiance of the received optical wave.

## Slide 20
MATHEMATICAL MODEL (contd.)
FSO |
20
(1.4)
(1.3)
where is obtained as,
exp
with the help of [21, Eq (5.5)], the integration in (1.3) yields
=
(1.5)
where is the Fox’s H-function.
Thus, the PDF of can be derived by

## Slide 21
MATHEMATICAL MODEL (contd.)
FSO |
21
To avoid dealing with the Fox's H-function, we have expanded it into an infinite power series by using [22, Th.1.4], and therefore obtain the series representation form of the double GG PDF:
(1.6)
Where,
(1.7)
=
=
(1.8)

## Slide 22
MATHEMATICAL MODEL (contd.)
FSO |
22
For RC MIMO FSO system involving lasers and photodetectors, the expression for post detection SNR is:
POST DETECTION ELECTRICAL SNR FOR RC MIMO
...(1.9)
Where, is the average electrical SNR and is the instantaneous channel fading coefficient between lasers and photodetector.
It is assumed that the ’s are independent and identically distributed (i.i.d.) random variates (RVs) with their PDFs following the same double GG distribution.

## Slide 23
MATHEMATICAL MODEL (contd.)
FSO |
23
Where,
AVERAGE SYMBOL ERROR RATE OF SUBCARRIER MPSK FOR MIMO FSO SYSTEM WITH RC SCHEME
From equation (1.6) and the assumption that have PDF following the same double GG distribution.
...(1.10)
=
...(1.11)
=
...(1.12)

## Slide 24
MATHEMATICAL MODEL (contd.)
FSO |
24
The Moment Generating Function (MGF) of can be derived in terms of power series:
...(1.14)
...(1.15)
...(1.13)
Using equation (1.10) and (1.13)

## Slide 25
MATHEMATICAL MODEL (contd.)
FSO |
25
From equation 3.478(1), Ref 24 we get,
Considering the first integral of equation (1.15),
...(1.16)
...(1.17)
Comparing equations (1.16) and (1.17), we get
...(1.18)
Now, equations (1.16) becomes:

## Slide 26
MATHEMATICAL MODEL (contd.)
FSO |
26
...(1.19)
...(1.20)
...(1.21)
Similarly, the second integral of equation (1.15) becomes:
Now equation (1.15) can be rewritten as:

## Slide 27
MATHEMATICAL MODEL (contd.)
FSO |
27
...(1.22)
...(1.23)
...(1.24)
Where
Now, let
...(1.25)
Since ’s are assumed to be i.i.d. RVs, MFG of Y can be expressed as:
...(1.26)

## Slide 28
MATHEMATICAL MODEL (contd.)
FSO |
28
...(1.27)
From equations (1.22) and (1.26),
...(1.28)
...(1.29)
By using Binomial Theorem, we get

## Slide 29
MATHEMATICAL MODEL (contd.)
FSO |
29
...(1.30)
By using equation 0.314, Ref. 24 we get,
...(1.31)
...(1.32)
Where
,
for and is a natural number
Using equation (1.29) and (1.30), we get

## Slide 30
MATHEMATICAL MODEL (contd.)
FSO |
30
...(1.33)
Where,
...(1.34)
...(1.35)
...(1.36)

## Slide 31
MATHEMATICAL MODEL (contd.)
FSO |
31
...(1.37)
From the principle of multiplication of infinite series,
...(1.38)
...(1.39)
Equation (1.32) can be rewritten as
From the definition of Inverse Laplace

## Slide 32
MATHEMATICAL MODEL (contd.)
FSO |
32
...(1.40)
From equation (8.315) Ref. 24, we get
...(1.41)
...(1.42)
From equations (1.38) and (1.39)

## Slide 33
MATHEMATICAL MODEL (contd.)
FSO |
33
...(1.43)
Substituting, in equation (2.42), we get
...(1.44)
By using equation (1.40), equation (1.44) can be rewritten as:

## Slide 34
MATHEMATICAL MODEL (contd.)
FSO |
34
...(1.45)
...(1.46)
...(1.47)

## Slide 35
MATHEMATICAL MODEL (contd.)
FSO |
35
...(1.48)
...(1.49)
...(1.50)
Let represent a RV which depend on the channel fading whose pdf is and is given as,
...(1.51)
Substituting the values from equation (1.47) to equation (1.49) we get,

## Slide 36
MATHEMATICAL MODEL (contd.)
FSO |
36
...(1.52)
...(1.53)
...(1.54)

## Slide 37
MATHEMATICAL MODEL (contd.)
FSO |
37
...(1.55)
...(1.56)
...(1.57)
Now, MFG of is given as,
Using equation (3.478(1)), Ref. 24 we get,

## Slide 38
MATHEMATICAL MODEL (contd.)
FSO |
38
...(1.58)
...(1.59)
Comparing equations (1.56) and (1.57) we get,
We get,
Therefore equation (1.56) becomes,

## Slide 39
MATHEMATICAL MODEL (contd.)
FSO |
39
...(1.60)
...(1.61)
Post detection electrical SNR for RC MIMO system (from equation (1.9)) is,
The average SER of subcarrier MPSK (from equation (19), Ref 1) is given as,
...(1.62)

## Slide 40
MATHEMATICAL MODEL (contd.)
FSO |
40
...(1.63)
...(1.64)
...(1.65)
Where,
Electrical SNR for RC MIMO system is,
Now, equation (1.63) becomes,
...(1.66)

## Slide 41
MATHEMATICAL MODEL (contd.)
FSO |
41
...(1.67)
...(1.68)
Substituting equations (1.60), (1.64), (1.65) in equation (1.63) we get

## Slide 42
MATHEMATICAL MODEL (contd.)
FSO |
42
...(1.69)
...(1.70)
Where,
On solving equation (1.69) in Mathematica we get,
Where,
2F1 is a Hypergeometric function.

## Slide 43
MATHEMATICAL MODEL(contd.)
FSO |
43
AVERAGE SYMBOL ERROR RATE FOR HYBRID LPPM-MPSK-SIM
...(1.71)
...(1.72)
The general expression for BER of coherent MPSK is
For M>4 and
For MPSK the BER expression is
...(1.73)
PROPOSED MODEL

## Slide 44
P=Q()
=
=
=
Where
MATHEMATICAL MODEL (contd.)
Where =modulation index , R=responsivity of photodetector
From equations (1.74) and (1.76) we get
From equations (1.74) and (1.78) we get
Where
...(1.75)
...(1.74)
...(1.77)
...(1.76)
...(1.79)
...(1.78)

## Slide 45
MATHEMATICAL MODEL (contd.)
We have
=
From equations (1.79) and (1.80) we get
=
Putting R=1,A=1 and =1 in equation (1.81) and then putting in equation we get conditional
BER of LPPM-BPSK
Similarly conditional BER expression of LPPM-MPSK-SIM is
The unconditional BER expression of LPPM-BPSK-SIM
=
...(1.81)
...(1.80)
...(1.83)
...(1.82)
...(1.84)
...(1.85)

## Slide 46
MATHEMATICAL MODEL (contd.)
Putting in equation (1.85) we get
Where
We have
From equations (1.87) and (1.89) we get
d
d
Where
d
...(1.87)
...(1.86)
...(1.89)
...(1.88)
...(1.91)
...(1.90)
...(1.92)
...(1.93)

## Slide 47
MATHEMATICAL MODEL (contd.)
The unconditional BER expression of LPPM-MPSK-SIM
=
Putting in equation (1.96) we get
We have
Where
...(1.95)
...(1.94)
...(1.96)
...(1.97)
...(1.98)
...(1.100)
...(1.99)

## Slide 48
MATHEMATICAL MODEL (contd.)
d
Where
AVERAGE SYMBOL ERROR RATE FOR HYBRID LPPM-BPSK-SIM FOR SISO SYSTEM
The Average SER expression of LPPM-MPSK-SIM
d
Where
From equation (1.22) we get
...(1.102)
...(1.101)
...(1.104)
...(1.103)
...(1.105)

## Slide 49
MATHEMATICAL MODEL (contd.)
From equations (1.103) and (1.105) the average SER of LPPM-BPSK-SIM for SISO is
Where
=
=
...(1.107)
...(1.106)
...(1.109)
...(1.108)
...(1.110)

## Slide 50
MATHEMATICAL MODEL (contd.)
AVERAGE SYMBOL ERROR RATE FOR HYBRID LPPM-MPSK-SIM FOR SISO SYSTEM
The Average SER expression of LPPM-MPSK-SIM
Where
From equation (1.22) we get
d
From equations (1.111) and (1.113) the average SER of LPPM-BPSK-SIM for SISO is
...(1.112)
...(1.111)
...(1.113)

## Slide 51
MATHEMATICAL MODEL (contd.)
=
Where
=
...(1.114)
...(1.116)
...(1.115)
...(1.117)
...(1.118)

## Slide 52
AVERAGE SYMBOL ERROR RATE FOR HYBRID LPPM-BPSK-SIM FOR MIMO SYSTEM
MATHEMATICAL MODEL (contd.)
The Average SER expression of LPPM-BPSK-SIM
d
Where
From equations (1.32) we get
(s)=
From equations (1.119) and (1.121) the average SER of LPPM-BPSK-SIM for MIMO is
...(1.120)
...(1.119)
...(1.121)

## Slide 53
MATHEMATICAL MODEL (contd.)
= d
= d
=
=
Where
...(1.123)
...(1.122)
...(1.125)
...(1.124)

## Slide 54
MATHEMATICAL MODEL (contd.)
AVERAGE SYMBOL ERROR RATE FOR HYBRID LPPM-BPSK-SIM FOR MIMO SYSTEM
The Average SER expression of LPPM-BPSK-SIM
Where
From equation (1.32) we get
From equations (1.126) and (1.128) the average SER of LPPM-BPSK-SIM for MIMO is
d
(s)=
...(1.127)
...(1.126)
...(1.128)

## Slide 55
MATHEMATICAL MODEL (contd.)
= d
= d
=
=
Where
...(1.130)
...(1.129)
...(1.131)
...(1.132)

## Slide 56
FSO |
56
RESULT AND ANALYSIS
Fig 1.2 SER of MPSK SIM for MIMO FSO system with RC over double GG fading under weak turbulence with .
It is observed that for 45 dB average electrical SNR, the corresponding values of average SER are , , , and for BPSK, 4-PSK, 8-PSK, and 16-PSK respectively.
Parameters Used:

## Slide 57
RESULT AND ANALYSIS(contd.)
Fig 1.3 SER of MPSK SIM for MIMO FSO system with RC over double GG fading under moderate turbulence with = 2.
It is observed that for 45 dB average electrical SNR, the corresponding values of average SER are 1.535 × 10−10, 1.628 × 10−9, 3.373 × 10−8 , and 9.27 × 10−7 for BPSK, 4-PSK, 8-PSK, and 16- PSK respectively.
Parameters Used:

## Slide 58
RESULT AND ANALYSIS(contd.)
Fig 1.4 SER of MPSK SIM for MIMO FSO system with RC over double GG fading under strong turbulence with = 25.
It is observed that for 45 dB average electrical SNR, the corresponding values of average SER are 4.067×10−5, 0.0001837 , 0.0009708 and 0.005925 for BPSK, 4-PSK, 8-PSK, and 16-PSK respectively
Parameters Used:

## Slide 59
RESULT AND ANALYSIS(contd.)
Fig 1.5 SER of BPSK SIM for MIMO FSO system with RC for three different laser-photodetector combinations under moderate turbulence with =2.
It is observed that for 45 dB average electrical SNR, the corresponding values of average SER are 8.351 ×10−10, 1.535 ×10−10, and 2.823 ×10−11 for 𝑛𝑇=4, 𝑛𝑅=1, 𝑛𝑇=2, 𝑛𝑅=2, and 𝑛𝑇=1, 𝑛𝑅=4 respectively.
Parameters Used:

## Slide 60
RESULT AND ANALYSIS(contd.)
Fig 1.6 SER of 4-PSK SIM for MIMO FSO system with RC for three different laser-photodetector
combinations under moderate turbulence with = 2.
It is observed that for 45 dB average electrical SNR, the corresponding values of average SER are 8.871 × 10−9, 1.628 × 10−9, and 2.991 × 10−10 for 𝑛𝑇 = 4, 𝑛𝑅 = 1, 𝑛𝑇 = 2, 𝑛𝑅 = 2, and 𝑛𝑇 = 1, 𝑛𝑅 = 4 respectively.
Parameters Used:

## Slide 61
RESULT AND ANALYSIS(contd.)
Fig 1.7 SER of 8-PSK SIM for MIMO FSO system with RC for three different laser-photodetector combinations under
moderate turbulence with = 2
It is observed that for 45 dB average electrical SNR, the corresponding values of average SER are 1.848×10−7, 3.373×10−8, and 6.179×10−9 for 𝑛𝑇=4, 𝑛𝑅=1, 𝑛𝑇=2, 𝑛𝑅=2, and 𝑛𝑇=1, 𝑛𝑅=4 respectively.
Parameters Used:

## Slide 62
RESULT AND ANALYSIS(contd.)
Fig 1.8 SER of 16-PSK SIM for MIMO FSO system with RC for three different laser-photodetector combinations under moderate turbulence with =2.
It is observed that for 45 dB average electrical SNR, the corresponding values of average SER are 5.173×10−6, 9.27×10−7, and 1.681×10−7 for 𝑛𝑇=4, 𝑛𝑅=1, 𝑛𝑇=2, 𝑛𝑅=2, and 𝑛𝑇=1, 𝑛𝑅=4 respectively.
Parameters Used:

## Slide 63
RESULT AND ANALYSIS(contd.)
Fig 1.9 SER of 4PPM MPSK SIM for SISO FSO system over double GG fading under moderate turbulence with =2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 0.002003, 0.002186, and 0.003073 for 4PPM 4PSK SIM, 4PPM 8PSK SIM, and 4PPM 16PSK SIM respectively
Parameters Used:

## Slide 64
RESULT AND ANALYSIS(contd.)
Fig 1.10 SER of 8PPM MPSK SIM for SISO FSO system over double GG fading under moderate turbulence with = 2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 0.001032, 0.001131, and 0.001602 for 8PPM 4PSK SIM, 8PPM 8PSK SIM, and 8PPM 16PSK SIM respectively.
Parameters Used:

## Slide 65
RESULT AND ANALYSIS(contd.)
Fig 1.11 SER of 16PPM MPSK SIM for SISO FSO system over double GG fading under moderate turbulence with = 2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 0.0005696, 0.0006253, and 0.0008895 for 16PPM 4PSK SIM, 16PPM 8PSK SIM, and 16PPM 16PSK SIM respectively.
Parameters Used:

## Slide 66
RESULT AND ANALYSIS(contd.)
Fig 1.12 SER of LPPM 4PSK SIM for SISO FSO system over double GG fading under moderate turbulence with =2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 0.002003, 0.001032, and 0.0005696 for 4PPM 4PSK SIM, 8PPM 4PSK SIM, and 16PPM 4PSK SIM respectively.
Parameters Used:

## Slide 67
RESULT AND ANALYSIS(contd.)
Fig 1.13 SER of LPPM 8PSK SIM for SISO FSO system over double GG fading under moderate turbulence with = 2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 0.002186, 0.001131, and 0.0006253 for 4PPM 8PSK SIM, 8PPM 8PSK SIM, and 16PPM 8SPK SIM respectively.
Parameters Used:

## Slide 68
RESULT AND ANALYSIS(contd.)
Fig 1.14 SER of LPPM 16PSK SIM for SISO FSO system over double GG fading under moderate turbulence with = 2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 0.003073, 0.001602, and 0.0008895 for 4PPM 16PSK SIM, 8PPM 16PSK SIM, and 16PPM 16PSK SIM respectively.
Parameters Used:

## Slide 69
RESULT AND ANALYSIS(contd.)
Fig 1.15 SER of 4PPM MPSK SIM for MIMO FSO system over double GG fading under moderate turbulence with =2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 5.736×10−9, 3.337×10−8, and 4.592×10−7 for 4PPM 4PSK SIM, 4PPM 8PSK SIM, and 4PPM 16PSK SIM respectively.
Parameters Used:

## Slide 70
RESULT AND ANALYSIS(contd.)
Fig 1.16 SER of 8PPM MPSK SIM for MIMO FSO system over double GG fading under moderate turbulence with = 2
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 3.472 × 10−10, 1.874 × 10−9, and 2.256 × 10−8 for 8PPM 4PSK SIM, 8PPM 8PSK SIM, and 8PPM 16PSK SIM respectively.
Parameters Used:

## Slide 71
RESULT AND ANALYSIS(contd.)
Fig 1.17 SER of 16PPM MPSK SIM for MIMO FSO system over double GG fading under moderate turbulence with = 2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 2.995×10−11, 1.554×10−10, and 1.723×10−9 for 16PPM 4PSK SIM, 16PPM 8PSK SIM, and 16PPM 16PSK SIM respectively.
Parameters Used:

## Slide 72
RESULT AND ANALYSIS(contd.)
Fig 1.18 SER of LPPM 4PSK SIM for MIMO FSO system over double GG fading under moderate turbulence with =2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 5.736×10−9, 3.472×10−10, and 2.995×10−11 for 4PPM 4PSK SIM, 8PPM 4PSK SIM, and 16PPM 4PSK SIM respectively.
Parameters Used:

## Slide 73
RESULT AND ANALYSIS(contd.)
Fig 1.19 SER of LPPM 8PSK SIM for MIMO FSO system over double GG fading under moderate turbulence with = 2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 5.736×10−9, 3.472×10−10, and 2.995×10−11 for 4PPM 4PSK SIM, 8PPM 4PSK SIM, and 16PPM 4PSK SIM respectively.
Parameters Used:

## Slide 74
RESULT AND ANALYSIS(contd.)
Fig 1.20 SER of LPPM 16PSK SIM for MIMO FSO system over double GG fading under moderate turbulence with = 2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 4.592×10−7, 2.256×10−8, and 1.723×10−9 for 4PPM 16PSK SIM, 8PPM 16PSK SIM, and 16PPM 16PSK SIM respectively.
Parameters Used:

## Slide 75
RESULT AND ANALYSIS(contd.)
Fig 1.21 SER of BPSK, 4PSK, 16PPM BPSK SIM, and 16PPM 4PSK SIM for MIMO FSO system over double GG fading under moderate turbulence with =2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 1.535×10−10, 1.628×10−9, 4.434×10−12, and 2.831×10−11 for BPSK, 4PSK, and 16PPM BPSK SIM, 16PPM 4PSK SIM respectively
Parameters Used:

## Slide 76
RESULT AND ANALYSIS(contd.)
Fig 1.22 SER of 16PPM 4PSK SIM, 16PPM 8PSK SIM for both SISO and MIMO FSO system over double GG fading under moderate turbulence with =2.
It is observed that for the average electrical SNR of 45 dB, the corresponding values of average SER are 0.0005696, 2.995×10−11, 0.0006253, and 1.554×10−10 for 16PPM 4PSK SIM SISO, 16PPM 4PSK SIM MIMO, 16PPM 8PSK SIM SISO, and 16PPM 8PSK SIM MIMO respectively.
Parameters Used:

## Slide 77
CONCLUSION
We have modelled the FSO channel using Double Generalized Gamma (GG) distribution under moderate turbulence condition.
We have proposed a new hybrid SIM with LPPM and MPSK and analyzed the SER.
We analyzed the average SER performance of MPSK and hybrid LPPM-MPSK-SIM over double generalized gamma fading under moderate turbulence condition, mathematically as well as using the MATLAB.
New hybrid Modulation can be further used with spatial diversity techniques to improve the FSO system performance.
It can also be applied to other channel models under all ranges of turbulence conditions.

## Slide 78
PUBLICATION

## Slide 79
FSO |
79
REFERENCES
Yi, X., Yao, M. and Wang, X., 2017. MIMO FSO communication using subcarrier intensity modulation over double generalized gamma fading. Optics Communications, 382, pp.64-72.
Kashani, M.A., Uysal, M. and Kavehrad, M., 2015. A novel statistical channel model for turbulence-induced fading in free-space optical systems. Journal of Lightwave Technology, 33(11), pp.2303-2312.
Liu, H., Liao, R., Wei, Z., Hou, Z. and Qiao, Y., 2015. BER analysis of a hybrid modulation scheme based on PPM and MSK subcarrier intensity modulation. IEEE Photonics Journal, 7(4), pp.1-10.
Giri, R.K. and Patnaik, B., 2019. Bit error rate performance analysis of hybrid subcarrier intensity modulation-based FSO with spatial diversity in various weather conditions. Journal of Optical Communications, 40(3), pp.307-314.

## Slide 80
FSO |
80
REFERENCES (contd.)
AlQuwaiee, H., Ansari, I.S. and Alouini, M.S., 2016. On the maximum and minimum of double generalized gamma variates with applications to the performance of free-space optical communication systems. IEEE Transactions on Vehicular Technology, 65(11), pp.8822-8831.
Kashani, M.A., Uysal, M. and Kavehrad, M., 2015, June. On the performance of MIMO FSO communications over double generalized gamma fading channels. In 2015 IEEE International Conference on Communications (ICC) (pp. 5144-5149). IEEE.
Aminikashani, M., Kavehrad, M. and Gu, W., 2016, February. Error performance analysis of FSO links with equal gain diversity receivers over double generalized gamma fading channels. In Broadband Access Communication Technologies X (Vol. 9772, p. 97720R). International Society for Optics and Photonics.

## Slide 81
FSO |
81
REFERENCES (contd.)
Jagadeesh, V.K., Palliyembil, V., Muthuchidambaranathan, P. and Bui, F.M., 2015. Free space optical communication using subcarrier intensity modulation through generalized turbulence channel with pointing error. Microwave and Optical Technology Letters, 57(8), pp.1958-1961.
Bhatnagar, M.R. and Ghassemlooy, Z., 2016. Performance analysis of gamma–gamma fading FSO MIMO links with pointing errors. Journal of Lightwave technology, 34(9), pp.2158-2169.
Li, J., Liu, J.Q. and Taylor, D.P., 2007. Optical communication using subcarrier PSK intensity modulation through atmospheric turbulence channels.
Kaur, P., Jain, V.K. and Kar, S., 2015. Performance analysis of free space optical links using multi-input multi-output and aperture averaging in presence of turbulence and various weather conditions. IET Communications, 9(8), pp.1104-1109.

## Slide 82
FSO |
82
REFERENCES (contd.)
Saeed, R.A. and Abbas, E.B., 2018, August. Performance Evaluation of MIMO FSO Communication with Gamma-Gamma Turbulence Channel using Diversity Techniques. In 2018 International Conference on Computer, Control, Electrical, and Electronics Engineering (ICCCEEE) (pp. 1-5). IEEE.
Johnsi, A.A. and Saminadan, V., 2013, April. Performance of diversity combining techniques for fso-mimo system. In 2013 International Conference on Communication and Signal Processing (pp. 479-483). IEEE.
Saber, M.J. and Keshavarz, A., 2018, May. On performance of adaptive subcarrier intensity modulation over generalized FSO links. In Electrical Engineering (ICEE), Iranian Conference on (pp. 358-361). IEEE.
Sadiku, M.N., Musa, S.M. and Nelatury, S.R., 2016. Free space optical communications: An overview. European scientific journal, 12(9).

## Slide 83
FSO |
83
REFERENCES (contd.)
Vellakudiyan, J., Muthuchidambaranathan, P., Bui, F.M. and Palliyembil, V., 2015. Performance of a subcarrier intensity modulated differential phase-shift keying over generalized turbulence channel. AEU-International Journal of Electronics and Communications, 69(11), pp.1569-1573.
Dabiri, M.T., Sadough, S.M.S. and Khalighi, M.A., 2017. FSO channel estimation for OOK modulation with APD receiver over atmospheric turbulence and pointing errors. Optics Communications, 402, pp.577-584.
Kaur, G., Singh, H. and Sappal, A.S., 2017. Free space optical using different modulation techniques—a review. International Journal of Engineering Trends and Technology (IJETT), 43(2).
Popoola, W.O. and Ghassemlooy, Z., 2009. BPSK subcarrier intensity modulated free-space optical communications in atmospheric turbulence. Journal of Lightwave technology, 27(8), pp.967-973.

## Slide 84
FSO |
84
REFERENCES (contd.)
Prabu, K. and Kumar, D.S., 2015. BER analysis for BPSK based SIM–FSO communication system over strong atmospheric turbulence with spatial diversity and pointing errors. Wireless Personal Communications, 81(3), pp.1143-1157.
Chatzidiamantis, N.D., Karagiannidis, G.K., Kriezis, E.E. and Matthaiou, M., 2011, June. Diversity combining in hybrid RF/FSO systems with PSK modulation. In 2011 IEEE International Conference on Communications (ICC) (pp. 1-6). IEEE.
Sasiela, R.J., 2007, May. Electromagnetic wave propagation in turbulence: evaluation and application of Mellin transforms. SPIE.
Kilbas, A.A., 2004. H-transforms: Theory and Applications. CRC Press.
Gradshteyn, I.S. and Ryzhik, I.M., 2014. Table of integrals, series, and products. Academic press.

## Slide 85
FSO |
85
REFERENCES (contd.)
Ting Jiang and Lin Zhao ,2019. Performance Improvement for Mixed RF–FSO Communication System by Adopting Hybrid Subcarrier Intensity Modulation. Article in MDPI Appl. Sci. 2019, pp 9, 3724-3724.
Marvin K. Simon and Mohamed-Slim Alouini , Digital Communication over Fading Channels
Faridzadeh, M., Gholami, A., Ghassemlooy, Z. and Gatri, A., 2014, September. BPSK-SIM-PPM modulation for free space optical communications. In 7'th International Symposium on Telecommunications (IST'2014) (pp. 794-798). IEEE.
Faridzadeh, M., Gholami, A., Ghassemlooy, Z. and Rajbhandari, S., 2012, July. Hybrid 2-PPM-BPSK-SIM with the spatial diversity for free space optical communications. In 2012 8th International Symposium on Communication Systems, Networks & Digital Signal Processing (CSNDSP) (pp. 1-5). IEEE.

## Slide 86
REFERENCES (contd.)
Tiwari, Pawan, Nikhil Kumar, Pragati Singh, Chhavi Srivastava, M. Lakshmanan, Piyush Jain, and Saurabh Katiyar. "Modeling and Analysis of Hybrid SIM with LPPM and MSK over Double Generalized Gamma Distribution in Free Space Optical Communication System." In 2019 International Conference on Vision Towards Emerging Trends in Communication and Networking (ViTECoN), pp. 1-4. IEEE, 2019.
Lu, J., Letaief, K.B., Chuang, J.I. and Liou, M.L., 1999. M-PSK and M-QAM BER computation using signal-space concepts. IEEE Transactions on communications, 47(2), pp.181-184.
Ghassemlooy, Z. and Popoola, W.O., 2010. Terrestrial free-space optical communications. Mobile and Wireless Communications Network layer and circuit level design, pp.355-392.

## Slide 87
THANK YOU!
87
FSO |
FOR YOUR ATTENTION